## Slide 1
IoT-ENABLED
Plant Growth & Environment Monitoring System
ESP32 • Sensors • Automated Irrigation • Real-time Monitoring
PROJECT PRESENTATION
Prepared by: Kalyan Kumar

## Slide 2
Project Overview
A sensor-based system to observe plant conditions and support timely watering.
02
What it does
Collects soil moisture, temperature, humidity and rain-sensor readings using an ESP32.
Why it matters
Helps reduce manual checking and supports more consistent plant care.
Core outcome
Can activate a relay-controlled pump when soil is dry and rain is not detected.
Project concept
Sensors → ESP32 controller → Decision logic → Relay / pump → Display or dashboard

## Slide 3
Problem Statement & Objectives
The project focuses on simple, low-cost monitoring and irrigation assistance.
03
Problem
Manual watering may happen too early or too late.
Soil and weather conditions can change during the day.
Frequent physical checking can be inconvenient.
Objectives
Read environmental sensor values.
Identify dry-soil conditions using a calibrated threshold.
Control a pump through a relay with safety limits.
Display readings for monitoring and testing.

## Slide 4
System Architecture
High-level data flow from sensing to action.
04
SENSORS
Soil moisture DHT22 Rain sensor
CONTROLLER
ESP32 Read & process sensor values
DECISION
Threshold logic Dry soil + no rain
OUTPUT
Relay module Water pump LCD / dashboard
Optional: Wi-Fi can be used to send readings to a cloud dashboard when implemented.

## Slide 5
Hardware Components
Main components used in the proposed prototype.
05
ESP32
Microcontroller with Wi-Fi and ADC inputs.
Soil moisture sensor
Measures a soil-related analog value.
DHT22
Measures air temperature and humidity.
Rain sensor
Provides a wet/dry-related signal.
Relay + water pump
Switches the pump using a suitable external supply.
LCD / optional PIR
Displays readings; PIR can detect motion if used.

## Slide 6
Software & Tools
Tools used to write, upload and observe the embedded program.
06
Arduino IDE
Used to edit and upload the ESP32 sketch.
Embedded C / C++
Implements sensor reading, threshold logic and relay control.
Serial Monitor
Shows sensor values and status messages for debugging.
Optional extensions
Blynk or ThingSpeak dashboard
Data logging and charts
Wi-Fi alerts

## Slide 7
Working Principle
Typical control sequence; calibrate thresholds for the actual sensors.
07
01
Sense
Read soil, temperature, humidity and rain values.
02
Evaluate
Compare readings with configured thresholds.
03
Decide
If soil is dry and rain is not detected, request watering.
04
Act safely
Switch relay and stop the pump after a maximum run time.
05
Observe
Display values in Serial Monitor or on an optional LCD.

## Slide 8
Automation Logic & Safety
Illustrative logic in the starter sketch; confirm behavior on your own modules.
08
Pump start condition
Soil reading indicates dry soil AND rain sensor indicates no rain AND pump is currently off AND cooldown has completed
Basic safeguards
Maximum pump-on duration Cooldown between watering cycles Pump uses a separate rated supply Test relay logic before connecting the pump
Threshold values are examples, not universal values. Calibrate with dry and moist soil and with dry/wet rain-sensor conditions.

## Slide 9
Testing Plan & Expected Results
Record actual readings and observations during your prototype test.
09
Test condition | What to check | Record
Dry soil | Soil reading crosses dry threshold | Raw ADC value
Moist soil | Pump should remain off | Raw ADC value
Rain / wet sensor | Watering should be inhibited | Rain ADC value
DHT22 connected | Temperature and humidity display | °C and %
Pump timeout | Pump stops at configured time limit | Run duration
Do not claim measured results until you have tested the physical prototype.

## Slide 10
Benefits & Limitations
A practical prototype can be expanded as reliability and calibration improve.
10
Potential benefits
Less frequent manual checking
Consistent threshold-based watering
Modular and relatively low-cost design
Can be extended with a cloud dashboard
Current limitations
Sensor readings need calibration
No cloud dashboard unless added
Soil and pump requirements vary
Hardware wiring and power must be verified

## Slide 11
Future Scope
Possible improvements after the basic sensor-and-pump system is stable.
11
Cloud dashboard
Remote monitoring of live readings.
Historical data
Charts to understand moisture trends.
Notifications
Alerts for low moisture or sensor errors.
Smarter control
Use plant type, soil type and watering schedules.
Power efficiency
Optimize sampling and supply for long-term use.

## Slide 12
Conclusion
The IoT plant monitoring concept combines environmental sensing, ESP32 processing and relay-based irrigation control.
Successful implementation depends on correct wiring, sensor calibration, safe pump power and real-world testing.
THANK YOU
Questions?